## Slide 1: Karst Hydrogeology Global Trends in Instrumentation, Monitoring and Flow Modeling
Seminar 1: THURSDAY JuLY 25, 2019
(LEARNINGS FROM THE 27th international Karstological school)

## Slide 2: SESSION 1: KARST HYDROGEOLOGY – PAST, PRESENT AND FUTURE
Invited Lecture:
Karst Hydrogeology–Who, What, Why, Where, When & How (I. Sasowsky)
Structural control on water circulation in the Bossea karst system – Piedmont Italy
(A. Nannoni)
Comprehensive hydraulic and hydrochemical interpretation of a karst area in South Hungary
(K. Csondor)
The Châtaigniers cave (Ardèche, France): an indicator of Pleistocene variations and Combe d’Arc meander shortcut
(K. Genuite)
Karst Hydrogeology: The high-flow low-storage extreme in marble aquifers
(T. Faulkner)
Basin-scale conceptual groundwater flow model for carbonate regions
(A. Tóth)
Photo by: IKS ZASU

## Slide 3
Karst Hydrogeology
Who, What, Why, Where, When and How
(I. Sasowsky)
Photo by: IKS ZASU

## Slide 4
WHAT is a KARST HYDROGEOLOGICAL SYSTEM?
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
(Ford&Williams, 2007)

## Slide 5
WHAT is a KARST HYDROGEOLOGICAL SYSTEM?
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
EXTREME FLOW VARIABILITY!
http://tiny.cc/38m19y
http://tiny.cc/5fo99y

## Slide 6
WHERE IS IT OCCURING?
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
https://www.un-igrac.org
http://tiny.cc/ulo99y

## Slide 7
1893
1895
WHO?
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
WHEN?
Edourd- Alfred Martel
Jovan Cvijic
1921

## Slide 8
1981
1989
2007
1988
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
WHEN?

## Slide 9
WHY?
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
Where is the water coming from?
Where is it going?
How much water is there?
Is the water safe to drink?

## Slide 10
HOW?
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
SCALLOPS
PASSAGE MORPHOLOGY
CAVE MORPHOLOGY
(Palmer, 1991)
(White & Culver, 2012)
(Palmer, 1991)

## Slide 11
DYE TRACING
WATER WELL MONITORING
HOW?
https://pubs.usgs.gov
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
DATA LOGGERS
GPSForestry-suppliers.com

## Slide 12
http://tiny.cc/mil09y
Karst Hydrogeology – Who, What, Why, Where, When and How (I. Sasowsky)
CAVE DIVING

## Slide 13: SESSION 1: KARST HYDROGEOLOGY – PAST, PRESENT AND FUTURE
Invited Lecture:
Karst Hydrogeology–Who, What, Why, Where, When & How (I. Sasowsky)
Structural control on water circulation in the Bossea karst system – Piedmont Italy
(A. Nannoni)
Comprehensive hydraulic and hydrochemical interpretation of a karst area in South Hungary
(K. Csondor)
The Châtaigniers cave (Ardèche, France): an indicator of Pleistocene variations and Combe d’Arc meander shortcut
(K. Genuite)
Karst Hydrogeology: The high-flow low-storage extreme in marble aquifers
(T. Faulkner)
Basin-scale conceptual groundwater flow model for carbonate regions
(A. Tóth)
Photo by: IKS ZASU

## Slide 14: Structural control on water circulation in the Bossea karst system – Piedmont Italy
(A. Nannoni)
thegoldenscope.com
Notes: This paper is a study on the _____
Bossea Cave is home to an underground scientific laboratory that monitors cave air, radon concentration, cave fauna, and subterranean waters.
The objective of this study is to understand the relationship of the structural setting and the water flow path of the bossea karst system.

## Slide 15
Structural control on water circulation in the Bossea karst system – Piedmont Italy (A. Nannoni)
(Vigna et al., 2017)

## Slide 16
Structural control on water circulation in the Bossea karst system – Piedmont Italy (A. Nannoni)
Flow rates were found to remain constant which indicates a very stable baseflow.
Slow drips in the cave respond in a very quick manner to the rain events.
(Vigna et al., 2017)

## Slide 17
The Châtaigniers cave (Ardèche, France): an indicator of Pleistocene variations and Combe d’Arc meander shortcut
(K. Genuite)
www.tourist-paradise.com

## Slide 18
The Châtaigniers cave (Ardèche, France): an indicator of Pleistocene variations and Combe d’Arc meander shortcut (K. Genuite)
https://www.amusingplanet.com
How did the the river and the endokarst interacted during the river incision and the short-cutting process?
(Genuite et al., 2019 )

## Slide 19
The Châtaigniers cave (Ardèche, France): an indicator of Pleistocene variations and Combe d’Arc meander shortcut (K. Genuite)
(Genuite et al., 2019 )

## Slide 20: Karst Hydrogeology: The high-flow low-storage extreme in marble aquifers (T. Faulkner)

## Slide 21
Karst Hydrogeology: The high-flow low-storage extreme in marble aquifers (T. Faulkner)
Raggejavreraige Cave, Norway
(Faulkner, 2006)
http://tiny.cc/lov99y

## Slide 22: Comprehensive hydraulic and hydrochemical interpretation of a karst area in South Hungary
(K. Csondor)
https://www.tripadvisor.com.my
Photo Credit

## Slide 23
Comprehensive hydraulic and hydrochemical interpretation of a karst area in South Hungary (K. Csondor)

## Slide 24
Comprehensive hydraulic and hydrochemical interpretation of a karst area in South Hungary (K. Csondor)
(Erhardt et al, 2017)
Applied Methods: (Csondor, 2019)
Hydraulic Potential of the Fluid potential field (pressure elevation profile, tomography potential map)
Numerical Simulation (regional water flow)
Dissolution Experiments (using limestone tablets)
Stable Isotopes using Radon
(Erhardt, 2017)

## Slide 25: Basin Scale Conceptual Groundwater Flow Model for Carbonate Regions
http://tiny.cc/tdz19y
(A. Toth)

## Slide 26
Basin-scale model may be used where Classical Karst are not applicable.
(Kiraly, 1975)
THEORETICAL CONSIDERATIONS (Toth,2015)
Gravity-driven regional groundwater flow (GDRGF) and hydraulic continuity of thick carbonate ranges
Effects of scale dependence of permeability distribution on flow in karstified carbonate regions
Springs and other surface manifestations of flowing groundwater as validation tools for GDRGF in thick carbonates
Numerical representation of the hierarchy and pattern of GDRGF systems in carbonate ranges
Basin-scale conceptual groundwater flow model for carbonate regions (A. Tóth)

## Slide 27
Basin-scale conceptual groundwater flow model for carbonate regions (A. Tóth)
Application of the gravity-driven regional groundwater flow (GDRGF) concept to the hydrogeologically complex thick carbonate system of the Transdanubian Range, is justified based on the principle of hydraulic continuity.

## Slide 28
Basin-scale conceptual groundwater flow model for carbonate regions (A. Tóth)
Hydraulic continuity
Unconfined and confined parts handled as a system
Topography-driven regional groundwater flow
Same methods as for siliciclastic basins
TOTHIAN TYPE FLOW

## Slide 29: Acknowledgements
Notes: Coffee Break

## Slide 30: SESSION 2: MONITORING – INSTRUMENTATION AND DATA ANALYSIS
Invited Lecture: Monitoring of Karst Water – Method and Techniques (R. Benischke)
Attempt to characterize aquifer hydrodynamics with modern analytical tools using remote sensing data and on site monitoring – (Example of Mt. Miroč, Serbia) (V. Gajovič)
Water-rock interaction in Postojna Cave: Can we use stable isotopes as paleothermometer? (M. Lipar)
Interaction of air and water dynamics in deep caves of Mt. Velebit, Dinaric Karst , Croatia
(D. Paar)
Decreasing the unpredictability of karst aquifers – preliminary results of speleological and hydrological research in Učka cave system, Croatia (L. Kukuljan)
Karstic Conduits connectivity, natural and disturbed hydraulic behaviours of the multi-layered aquifer system of Barrois Limestone (H. Benabderrahmane)

## Slide 31
Monitoring of Karst Water Method and Techniques
(R. Benischke)

## Slide 32
MONITORING IS A PROGRAMMED PROCESS…
SURVEY/SCREENING short term program
SURVEILLANCE
continuous, special program of measurement

## Slide 33
Atmosphere – Watershed - Catchment
OUTPUT SYSTEM
Karst (springs, surface water)
Monitoring of Karst Water – Method and Techniques (R. Benischke)
WHAT TO MONITOR?
INPUT SYSTEM
Precipitation, Surface Runoff,
Surface Morphology, Recharge Conditions,
Soil cover, Geology, Vegetation, Anthropogenics,
http://tiny.cc/ggi69y

## Slide 34
HYDROMETEOROLOGIC PARAMETERS
Precipitation
Water Level
Water Flow Velocity
Air Temperature
Wind Parameters
Radiation Parameters
CHEMICAL AND PHYSICAL PARAMETERS
Inorganic and organic components (ions, PAH, undissociated components etc..)
Bulk parameters (electric conductivity, SAC)
Water Temperature
Turbidity, colour
Isotopes (stable, radiogenic)
Monitoring of Karst Water – Method and Techniques (R. Benischke)
Biological PArameters
Macro-zoobenthos
Microbiology
Enzymatic activity …
WHAT TO MEASURE?
HYDROMETEOROLOGIC PARAMETERS

## Slide 35
Parameter | Manual | Online | Instrument | Logger | Sampling
Precipitation |  |  | Rain gauge, weighing, etc. |  | 
Air temperature |  |  | Handheld, probe |  | 
Stage |  |  | Height gauge |  | 
Flow Rate |  |  | Current meter, tracer, ADV |  | 
Water Temperature |  |  | Handheld, probe |  | 
Rel. Conductivity |  |  | Handheld, probe |  | 
pH-Value |  |  | Handheld, probe |  | 
Turbidity |  |  | Handheld, probe, UV/VIS |  | 
SAC |  |  | Handheld, probe, UV/VIS |  | 
O2 |  |  | Handheld, amperometry, fluorescence quenching |  | 
Cations |  |  | Handheld, ion-selective probe |  | 
Anions (no alkalinity) |  |  | Handheld, ion-selective prove, UV/VIS |  | 
Alkalinity |  | extensive | Manual titration, titrator |  | 
Flourescence |  | extensive | Field or lab fluorometer |  | 
Radioisotopes |  | extensive | Field-probe or lab instrument |  | 
Stable Isotopes |  | extensive | Field-probe or ab instrument |  | 
Microbiology |  | extensive | Field-probe or lab instrument, cytometry |  | 
Monitoring of Karst Water – Method and Techniques (R. Benischke)

## Slide 36
Monitoring of Karst Water – Method and Techniques (R. Benischke)
PARAMETER AND SENSOR SELECTION
Selectivity for reliable Data
Sensivity fo accurate Data
No Cross-sensitivity with other parameters
High temporal and spatial resolution
Robustness of individual sensors and sensor networks for rough field conditions
Long-term stability to minimize maintenance work and costs
Cheap and easy to operate sensors
(Kluge et al. (2008)

## Slide 37
WHERE TO SAMPLE?
https://quaternary.uibk.ac.at/Methods/Cave-Monitoring.aspx
Monitoring of Karst Water – Method and Techniques (R. Benischke)

## Slide 38
https://quaternary.uibk.ac.at/Methods/Cave-Monitoring.aspx
HOW LONG TO OBSERVE?
Monitoring of Karst Water – Method and Techniques (R. Benischke)

## Slide 39
UNDER WHAT CONDITIONS?
Monitoring of Karst Water – Method and Techniques (R. Benischke)
(Kluge et al., 2010).

## Slide 40: SESSION 2: MONITORING – INSTRUMENTATION AND DATA ANALYSIS
Invited Lecture: Monitoring of Karst Water – Method and Techniques (R. Benischke)
Attempt to characterize aquifer hydrodynamics with modern analytical tools using remote sensing data and on site monitoring – (Example of Mt. Miroč, Serbia) (V. Gajovič)
Water-rock interaction in Postojna Cave: Can we use stable isotopes as paleothermometer? (M. Lipar)
Interaction of air and water dynamics in deep caves of Mt. Velebit, Dinaric Karst , Croatia
(D. Paar)
Decreasing the unpredictability of karst aquifers – preliminary results of speleological and hydrological research in Učka cave system, Croatia (L. Kukuljan)
Karstic Conduits connectivity, natural and disturbed hydraulic behaviours of the multi-layered aquifer system of Barrois Limestone (H. Benabderrahmane)

## Slide 41: Attempt to characterize aquifer hydrodynamics with modern analytical tools using remote sensing data and on-site monitoring – (Example of Mt. Miroč, Serbia)
(V. Gajovič)
http://www.panacomp.net/miroc-mountain/

## Slide 42
Attempt to characterize aquifer hydrodynamics with modern analytical tools using remote sensing data and on site monitoring – (Example of Mt. Miroč, Serbia)
(V. Gajovič)
(Ljubojevic, 2001)

## Slide 43
Water-rock interaction in Postojna Cave: Can we use stable isotopes as Paleothermometer?
(M. Lipar)
https://twitter.com/postojnacave
Notes: In

## Slide 44
Water and rock interaction in Postojna Cave - Can we use stable isotopes for Paleothermometer? (M. Lipar)

## Slide 45
Water and rock interaction in Postojna Cave - Can we use stable isotopes for Paleothermometer? (M. Lipar)
http://tiny.cc/n69z9y
http://tiny.cc/s89z9y
http://tiny.cc/v99z9y
Use of Radiology CT-Xray of stalagmite to pre-screen samples

## Slide 46: Interaction of air and water dynamics in deep caves of Mt. Velebit, Dinaric Karst , Croatia
(D. Paar)
http://www.panacomp.net/miroc-mountain/

## Slide 47
http://speleologija.eu/lukinajama
Interaction of air and water dynamics in deep caves in Mt. Velebit, Dinaric Karst, Croatia (D. Paar)
http://speleologija.eu/lukinajama
Develop model of cave air situation to understand the presence of perennial ice and interaction of water and other physical processes.

## Slide 48
Interaction of air and water dynamics in deep caves in Mt. Velebit, Dinaric Karst, Croatia (D. Paar)
(Stroj & Paar, 2018)

## Slide 49
Interaction of air and water dynamics in deep caves in Mt. Velebit, Dinaric Karst, Croatia (D. Paar)
(Stroj & Paar, 2018)

## Slide 50: Decreasing the unpredictability of karst aquifers – preliminary results of speleological and hydrological research in Učka cave system, Croatia
(L. Kukuljan)

## Slide 51
Decreasing the unpredictability of karst aquifers – prelim results of speleological and hydrological research in Učka cave system, Croatia (L. Kukuljan)
A Hydrological and microclimate monitoring was established in Ucka cave in 2018
Preliminary results already came up mapping at least 4.1km of cave that goes to a depth of 427m.

## Slide 52: Karstic conduits connectivity, natural and disturbed hydraulic behaviours of the multi-layered aquifer system of Barrois Limestone
(H. Benabderrahmane)

## Slide 53
Karstic Conduits connectivity, natural and disturbed hydraulic behaviours of the multi-layered aquifer system of Barrois Limestone (H. Benabderrahmane)
The karstic geometry is modelled using a formulation of the stochastic differential equation of Langevin.

## Slide 54: Acknowledgements